## Slide 1
2009/1/6
1
Network & System Lab, NSYSU
Chapter 22: TCP Persist Timer
2009/1/6
Introduction
Why we use persist timer:
  If an acknowledgment is lost, we could end up with both sides waiting for the other
    To prevent deadlock from occurring the sender uses a persist timer
    The sender queries the receiver periodically to find out if the window has been increased. These segments from the sender are called window probes.
An Example:
  We’ll invoke the server as
    svr4 % sock -i -s -P100000 5555
  The server sleep for 100,000 seconds (27.8 hours) before reading from the network
  The client on host bsdi and performs 1024-byte writes to port 5555 on the server
2
為什麼TCP掉ack影響不大?
因TCP是累加ack

## Slide 2
2009/1/6
3
Network & System Lab, NSYSU
An Example
2009/1/6
Silly Window Syndrome
About persist timer:
  It always bounded between 5 and 60 seconds
  The persist state which is different from the retransmission timeout is that TCP never gives up sending window probes.
When it occurs small amounts of data are exchanged across the connection, instead of full-sized seqments.
What is Silly Window Syndrome
  It can be caused by either end:
    The receiver can advertise small windows
    The sender can transmit small amounts of data.
4
Window size都很小，

## Slide 3
2009/1/6
5
Network & System Lab, NSYSU
Silly Window Syndrome (Cont.)
Correct avoidance is performed on both ends:
  The receiver must not advertise small windows
  The sender is not transmitting unless one of conditions is true:
    A full-sized segment can be sent
    We can send at least one-half of the maximum sized window ever advertised
    We can send everything we have if:
      We are not expecting an ACK (no outstanding data), or
      The Nagle algorithm is disabled (W ≠ 1)
2009/1/6
Silly Window Syndrome
6

## Slide 4
2009/1/6
7
Network & System Lab, NSYSU
Silly Window Syndrome
2009/1/6
Summary
TCP’s persist timer is set by one end of a connection when it has data to send, but has been stopped because the other end has advertised a zero-sized window.
TCP’s avoidance of the silly window syndrome is to prevent TCP from advertising small windows or from sending small segments
8